Tehniskā specifikācija

Pielikums Nr.2

PIEGĀDĀJAMĀ TEHNIKAS APJOMS UN IETEICAMĀ SPECIFIKĀCIJA

VISĀM PIEGĀDĀTAJĀM IEKĀRTĀM UN PROGRAMMATŪRAI IR JĀBŪT SAVIETOJAMAI AR KULDĪGAS NOVADA PAŠVALDĪBAS POLICIJAS ESOŠO GEOVISION VIDEONOVĒROŠANAS SISTĒMU.

UZSTĀDĪŠANAS UN INSTALĒŠANAS DARBOS JĀPAREDZ ESOŠĀS SISTEMAS PIESLĒGŠANA PIEGĀDĀTĀJĀM IEKĀRTĀM

JA NEPIECIEŠAMA APSEKOŠANA SASKAŅOT- NORMUNDS ĶĪVĪTIS mob.tālr. 29478135 normunds.kivitis@kuldiga.lv

| Nr. | Nosaukums | Iteicamā specifikācija | TIPS | Mērv. |
| --- | --- | --- | --- | --- |
| 1. | Krāsu Speed Dome D/N IP kamera SNC-RX570/OUTKI (vai līdzvērtīga) | Image device: 1/4-type Exwave HAD CCD. Number of effective pixels: 440,000 (752 x 582) Electronic shutter: 1 to 1/10,000 s Gain control: Auto/Manual (-3 dB to +28 dB) Exposure control: Auto (Full auto, Shutter-priority, Iris-priority), Manual, EV compensation, Backlight compensation White balance mode: Auto, Indoor, Outdoor, One-push auto, ATW/Manual Lens type: Auto-focus zoom lens Zoom ratio: 36x optical zoom (432x with digital zoom) Horizontal viewing angle: 2.2 to 54.2 degrees Focal length: f=3.5 to 91.0 mm F-number: F1.6 (wide), F3.8 (tele) Minimum object distance: 320 mm (wide),1,500 mm (tele) Pan angle: 360 degree endless rotation Pan speed: 300 degree/s (max.) Tilt angle: -90 to 0 degrees Tilt speed: 300 degrees/s (max.) Other functions: Day/Night, Intelligent Motion Detection, Intelligent Object Detection, Anti-tampering, Image stabilizer, Position preset Image. Image size (H x V): 640 x 480, 320 x 240, 160 x 120 (JPEG, MPEG-4, H.264) Compression format: JPEG, MPEG-4, H.264 Maximum frame rate: JPEG/MPEG-4 : 25 fps (640 x 480) H.264 : 8 fps (640 x 480) Audio. Audio compression: G.711/G.726 (40, 32, 24, 16 Kb/s) Network. Protocols: TCP/IP, HTTP, ARP, ICMP, FTP, SMTP, DHCP, SNMP, DNS, NTP Number of clients: 20 Interface. Ethernet: 10Base-T/100Base-TX (RJ-45) Serial interface: RS-232C (Transparency function or VISCA protocol) Card slots: PC card x1, Memory Stick x1 Analog video output: BNC x1, 1.0 Vp-p, 75 Ω External microphone input: Mini-jack (monaural, 2.2 K2.5 V plug-in power) Audio line output: Mini-jack (monaural), max output level: 1 Vrms Analog video output. Signal system: PAL (Composite) Horizontal resolution: 460 TV lines S/N ratio: 50 dB Min. Illumination: Color: 1 lx (50IRE, F1.6, AGC ON), B/W: 0.15 lx (50IRE, F1.6, AGC ON) General. Power consumption: 25 W max. Operating temperature: 0 to 50 °C (32 to 122 °F) Storage temperature: -20 to 60 °C (-4 to 140 °F) Mass: 2.2 kg (4 lb 13 oz) Dimensions (W x H x D): 160 x 160 x 230 mm (6 3 /8 x 6 3 /8 x 9 1 /8 inches) Body color: Black Power requirements: AC 24 V/DC 12 V System requirements. Operating system: Microsoft Windows 2000/XP Processor: CPU: Intel Pentium IV 1.5 GHz or higher Memory: RAM: 256 MB or more Web browser: Microsoft Internet Explorer Ver.5.5 or 6.0 Supplied Accessories. Ceiling-mount bracket (A) Ceiling-mount bracket (B) Screws Wire rope CD-ROM (setup software) Operation manual Installation manual | IP grozāmā kamera | 1.gab. |
| 2. | IR (InfraRed) prožektors (100m-Outdoor efective range;60O; 220V) | 100m-Outdoor efective range;60O; 220V | Gaismas iekārta | 3.gab. |
| 3. | GV-HOT Swap 8bay Recording Server System(licence for 32CH) Max 128CH (vai līdzvērtīgs) | CPU: 2nd Generation Intel® Core™ i7 Processor. RAM: 8 GB Dual Channels. Drive Bay: 8 / 4 bays Operating System: 64-bit Microsoft Windows 7 Embedded. Backup Type: DVD+R (DL) / DVD-R (DL) / DVD+R / DVD+RW / DVD-R / DVD-RW / CD-R / CD-RW Recovery DVD: Automatic system rebuild. Connector: Ethernet: RJ-45, 10 / 100 / 1000 Mbps x 3 Monitor Output: DB-15 VGA Monitor Output, DVI-DL Output (DVI-D signal Only), HDMI Output USB 2.0 : Front : 2 ports, Rear : 6 ports USB 3.0 : Rear: 2 ports Remote Access: TCP/ IP, LAN, WAN, Internet, Modem Dial-up, Modem-to-Modem, ISDN Operating Temp.: 0 ~ 45 °C (32 ~113 °F) Humidity: 0 ~ 80% RH (non-condensing) Dimensions (W x H x D): 483 x 178 x 528 mm / 19 x 7 x 21 in Software Specifications. Number of IP Video Device Connections: 128 channels. Number of Remote Client Connections: 300 channels. Active Connections: Yes. Passive Connections: Yes (only for GV IP devices). 3rd Party IP Cameras Support : Yes. Live Viewing : Single live view, multi-channel live view. Recording: Yes (up to 128 channels) Protocol: HTTP, HTTPS, TCP, UDP, SMTP, UPnP, DynDNS, RTSP, PSIA, ONVIF. E-Mail Notification: Yes (for Active connection lost, passive connection lost, USB protection key removed, recycling of recorded video, start keep days operation, motion detection, disk full, disk error, I/O trigger, disk removed, recording failure). SMS Notification: No. 2-Way Audio: Yes (only for GV-IP devices through active connection) GPS support: Yes (only for GV-IP cameras) Number of Accounts : Up to 1000 accounts. Mobile Phone Support: No. Bandwidth Control: No. IE Live View : Yes (up to 36 channels). IE Event Query: Yes. IE I/O Control: No. Language: Multi Language. | Serveris | 1.gab. |
| 4. | GV-IP Control center software |  | Licence | 1.gab |
| 5. | HDD (Cietie diski) 2TB(with 20TB storage) | RPM 7200 SATA | Iekārtas | 8.gab. |
| 6. | Videoreģistrators(500W 14cm/H67 INTEL/i7-870/1TB_sv35x1Tb/DVDRW/2x2GB_DDR3/ Win7PRO64bit/Software Geovisio ar HD | Model: Video Input: GV‐NVR (GV): 32. GV‐NVR: 1, 2, 4, 6, 8, 10, 12, 14, 16, 18, 20, 22, 24, 26, 28, 30, 32; Audio Input: GV‐NVR (GV): 32. GV‐NVR: 1, 2, 4, 6, 8, 10, 12, 14, 16, 18, 20, 22, 24, 26, 28, 30, 32; Video Codec: MJPEG, MPEG4, H.264. Audio Codec: AAC (16 kHz / 16 bit). Video Resolution: From CIF to 5 Mega pixel. Networking: TCP / IP, LAN, WAN, Internet, Modem Dial‐up, Modem‐to‐Modem, ISDN. Backup Device: HDD, NAS, CD‐R / R‐W, DVD+R / +RW, DVD+R (DL), ZIP, JAZ, Blu‐ray, GV‐Storage System. Mobile Phone / PDA: Symbian S60 (2.X~3.X), Windows Mobile (5.0~6.1), Blackberry (4.2.1~4.7), iPhone (2.2~3.1) Language: Multi Language. | Sistēmbloks | 1.gab. |
| 7. | Keybords/joystick SNCA-JOYSTICK (vai līdzvērtīgs) | IP Dektop USB | Iekārta | 1.gab. |
| 8. | Video Server GV-VS04H H26 (vai līdzvērtīgs) | Video. Video Standard:NTSC,PAL. Video input: 4 channels Compression: H.264 Frame Rate(at Full D1 resolution) *NTSC:30 fps per channel;120 ps total for 4 channels*PAL :25 fps per channel; 100 fps in total for 4 channels. Resolution: *NTSC 704 x 480, 704 x 480 de‐interlace, 352 x 240, 176 x 112.* PAL 704 x 576, 704 x 576 de‐interlace, 352 x 288, 176 x 144. Video Streaming : Configurable frame rate and bandwidth, Constant and variable bitrate. Video Adjustment: Brightness, Contrast, Hue, Saturation. Audio. Audio Input: 4 channels. Compression: G.723 Management. Event Management: *Trigger: Schedule, Sensor Input, Motion Detection.* Action: Store video (AVI format), Send e‐mails with captured images, Upload captured images to FTP Server, Monitor through Center V2, VSM and GV‐GIS, Activate relay outputs to control external devices. Storage: Mass storage through USB (optional). Client PC Requirements: Microsoft IE 7.x or above running on Windows XP/ Vista / 7 / Server 2008. Security: IP address filtering. Language: Multi Language. Network. Interface: 10/100 Base‐T Ethernet, 802.11b/g, 802.11n Wireless LAN (optional) Mobile broadband: UMTS, EDGE, etc. (optional). Protocol: HTTP, HTTPS, TCP, UDP, SMTP, FTP, DHCP, NTP, UPnP, DynDNS, 3GPP/ISMA, Multicast, RTSP, QoS (DSCP), SNMP. Connector. Video Input: 4 BNC ports. Audio Input: 2 stereo phone jacks to 4 RCA ports. Audio Output: 1 RCA port. Sensor Input: 4 inputs. Alarm Output: 4 outputs. PTZ: RS‐485 +/‐. GPS: UART. Ethernet: RJ‐45, 10/100 Mbps. USB: 2 ports (USB 2.0). Power: Input: 100‐240V, 1.2A, 50‐60 mHz. Output: 12V, 3A, (36W Max.). Power over Ethernet. PoE Standard: IEEE 802.3af Power over Ethernet / PSE. PoE Power Supply Type: End‐Span PoE Power Output: Per Port 48V DC, 350mA. Max. 15.4 watts. Environment. Operation Temp.: ‐20 ~ 55 °C / ‐4 ~ 131 °F Humidity: 0 ~ 85% RH (non‐condensing). Physical. Dimensions (L x W x H): 174 x 145 x 40 mm / 6.85 x 5.7 x 1.57 in Weight: 0.73 kg / 1.61 lb. Applications Network Storage: GV‐System, GV‐Backup Center, GV‐Video Gateway, GV‐Recording Server Mobile Phone support: GV‐AView for Android Smartphone, GV‐Eye HD for iPad, GV‐Eye for iPhone and iPod Touch, GV‐GView for Windows PDA, GV‐MSView for Windows Smartphone, GV‐SSView for Symbian Smartphone, 3G‐enabled phone. Live Viewing: IE , GV‐Multi View CMS Server support: GV‐Control Center, GV‐Center V2, GV‐VSM | Iekārta anlogā video signāla konvertēšanai | 1.gab. |
| 9. | TV panelis ar sienas stiprinājumu –LG42LV3550 (vai līdzvērtīgs) | 42" (107cm) Black/ Full HD 1920x1080/ 500cdqm/ 60000:1/ 4ms/ USB (Mp3/Jpeg)/ DVB-C DVB-T (MPEG-4) | Iekārta video novērošanai | 1.gab. |
| 10. | 230V 50Hz Off-line UPS (NeTYS PE 1000(1000V) (vai līdzvērtīgs) |  | Iekārta | 1.gab. |
| 11. | Datu kabelis (ārējais) FTP 4x2x0,5 Cat5e | Ārējais FTP 4x2x0,5 Cat5e | Materiāli | apt.30m |
| 12. | Barošanas kabelis ārdarbiem 3x1,15mm | Ārdarbiem 3x1,15mm | Materiāli | apt.30m |
| 13. | Komunikāciju skapis 600x600x600 |  | Iekārta | 1.gab. |
| 14. | SWICH -koncentrators (Rackmountable Switch, 16 port 10/100/1000BASE-T, Gigabit Ethernet (Full-Duplex): 2000 Mbps) | Rackmountable Switch, 16 port 10/100/1000BASE-T, Gigabit Ethernet (Full-Duplex): 2000 Mbps) | Tīkla aprīkojums | 1.gab. |
| 15. | Citi materiāli lai nodrošinātu iekārtu pieslēgšanu UPS (Elektriskais pagarinātājs 6 viet., montējams skapī, barojams no UPS (var būt pielāgots) (, path kabeļi (CAT5E, UTP, RJ45/RJ45, lietais konektors), konektori(RJ/45), kabeļi monitoriem, TV-RGB -1 gab 2m,DVI-1. gab -2m) u.c. |  | Aprīkojums | gab. |

VEICAMIE DARBI

| Nr. |  | APRAKSTS | PIEZĪMES |
| --- | --- | --- | --- |
| 1. | IP grozāmās kameras uzstādīšana (1.gab) | Uzstādīt un pieslēgt elektrotīklam IP kameru uz Kuldīgas peldētavas glābšanas dienesta mājas(*) pie Ventas rumbas. Nodrošināt video signāla pārraidi izmantojot esošo WiFi tīklu izmantojot AP(access point) uz Valsts policijas torņa Liepājas ielā 26(**) līdz Kuldīgas pašvaldības policijai Strautu ielā 1 (***) | *Google maps aptuvenās koordinātes 56.968369,21.980551 ** Google maps aptuvenās koordinātes 56.968223,21.964888 *** Google maps aptuvenās koordinātes 56.967457,21.969779 Uztveršanas antēna atrodās uz Kuldīgas novada pašvaldības ēkas jumta Baznīcas ielā 1 un savienota ar Kuldīgas novada pašvaldības policijas ēku ar datu kabeli. KAMERAS DARBĪBAI JĀNODROŠINA MAKSIMĀLA VENTAS RUMBAS REDZAMĪBA, LAI NOVĒRSTU NELEGĀLO ZIVJU IEGUVI UN CITAS NELIKUMĪGAS DARBĪBAS. |
| 2. | IR(InfraRed) prožektoru uzstādīšana (3.gab) | Uzstādīt un pieslēgt elektrotīklam 3 IR prožektorus pa perimetru uz Kuldīgas peldētavas glābšanas dienesta mājas(*) pie Ventas rumbas. Nodrošinot attālinātu vadību caur starpreleju pieslēdzot pie IP kameras . | Uzstādīšanas vietas un virzienus aprēķināt , lai nodrošinātu kameras apgaismojumu diennnakts tumšajā laikā Ventas baseinā 180 grādos - |
| 3. | Video novērošanas sistēmas reorganizācija un pilnveidošana Kuldīgas novada pašvaldības policijā Strautu ielā 1 | Uzstādīt Kuldīgas novada pašvaldības policijas video novērošanas telpā Strautu ielā 1 Komunikāciju skapi ar elektrisko 6 vietīgo pagarinātāju (*) Skapī iemontēt GV-HOT Swap 8bay Recording Server – 1g , Video Server GV-VS04H H26 – 1. gab., SWICH –koncentrators – 1gb. Piestiprināt pie sienas TV paneli. Veikt instalācijas darbus –nodrošinot vienotas video novērošanas sitēmas izveidi izmantojot piegādāto tehniku un programmatūru (**). | *Skapi nobarot caur UPS iekārtu ** nodrošināt GeoVision un Video net sitēmu novērošanu kameru gan IP gan Analogo vienotu novērošanas un vadības sistēmu. |